## Slide 1: Molecular luminescence spectroscopy
Chemistry 243

## Slide 2: Luminescence
Emission of photons accompanying the relaxation from an excited to a ground state.
Photoluminescence—Excited state generated by absorption of a photon.
  Fluorescence and phosphorescence
Chemiluminescence—Chemical reaction generates excited state.
Luminescence methods have greater inherent sensitivity than absorbance and often have greater linear dynamic range.
Disadvantage is that not all molecules luminesce and matrix interferences are more significant.

## Slide 3: What’s spin got to do with it?
Fluorescence involves emission from states having the same spin.
  Lifetime 10-8-10-5 sec
Phosphorescence comes from “spin forbidden” transitions.
  Lifetime longer than 10-5 sec
  Seconds, minutes, hours
Emission maximum of fluorescence and phosphorescence typically at lower energy than excitation radiation—Stokes shift.
  Exception: resonant emission (atomic fluorescence)

## Slide 4: Molecular energy level diagrams aka Jablonski diagrams
phosphorescence > fluorescence
fluorescence > absorbance

## Slide 5: Quantum yield
A metric that describes efficiency of the fluorescent or phosphorescent process.
  Approaches 1 for highly luminescent molecules
  0 for non-luminescent molecules
Ratio of the number of luminescent molecules compared to the total number excited.
  Consider all deactivation pathways
kf = fluorescent rate constant
ki = intersystem crossing rate constant
kec = external conversion rate constant
kic = internal conversion rate constant
kpd = predissociation rate constant
kd = dissocation rate constant

## Slide 6: Transition type and effects on fluorescence and phosphorescence
s*-s transitions rarely result in luminescence
  Too high of energy (l < 250 nm) leads to predissociation and dissociation
Emission more common from p*-p, but also p*-n
  From the lowest excited state
p*-p usually has greater quantum efficiency
  Greater molar absorptivity of p-p* (10-100x) means high transition probability—short lifetime leads to large kf

## Slide 7: Structural considerations
Fluorescence common in aromatic compounds with low-energy *-  transitions
  Conjugation shifts emission to red and greatly increases f
    Example: pyridine vs. quinoline
Sensitive to substituents
  Wavelengths of maximum absorption and emission and quantum yield
  Halogens lead to sharp decreases in f
    Heavy atom effect promotes intersystem crossing via spin-orbit coupling
    Electronegativity also can give easily broken bonds
Structural rigidity enhances fluorescence
  Lack of rigidity promotes non-radiative decay pathways (kic)
    Example: Fluorene vs. biphenyl
vs.

## Slide 8: Environmental effects on fluorescence
Temperature
  Increased number of collisions promotes external conversion.
Solvent
  Heavy atoms in solvent promote intersystem crossing.
pH
  Differing protonation states lead to resonance structures that change excited state energies
Concentration
  When too many chromophores, the radiant power decreases through the sample so that not all species have chance to absorb and thus emit.

## Slide 9: Quenching of fluorescence and phosphorescence
Nonradiative energy transfer from excited states to other molecules.
Dynamic (collisional) quenching—external conversion
  Collision of excited species and quencher dependent on diffusion
    Temperature, viscosity, and quencher concentration-dependent
    Dissolved O2 is efficient quencher—degas solutions
Static quenching: quencher complexes with ground state fluorophore to form ‘dark complex’
Förster quenching
  Not dependent on collisions—long-range effect
  Dipole-dipole coupling—falls off as 1/(distance)6
  Basis for Fluorescence Resonance Energy Transfer (FRET)

## Slide 10: FRET microscopy
http://upload.wikimedia.org/wikipedia/commons/3/3a/FRET.PNG
http://www.bphys.uni-linz.ac.at/bioph/res/icg/Bilder/fret_methJD.png
http://www.moleculardevices.com/pages/MM-new/metamorph_applications.html
Nature Rev. Molec. Cell Biol., 2002, 3, 906-918.
Wild type
Mutant

## Slide 11: Excitation and emission spectra
quinine
A
B
C
D
A
B
C
D

## Slide 12: Instrumentation for fluorescence and phosphorescence
Almost always are double-beam
  To compensate for radiant power fluctuations
Right angle detection
Why?
Why?

## Slide 13: Components of fluorometers and spectrofluorometers
Sources
  Most common: Low-pressure Hg vapor lamps
    254, 302, 313, 546, 578, 691, and 773 nm lines
  High-pressure Xe lamps
    Continuum from 300-1300 nm
  Lasers: essential for research operation with small samples, remote sensing (collimation), and when highly monochromatic light needed
Wavelength selectors
  Interference filters or absorption filters for fluorometers
  Grating monochromators (usually two) in spectrofluorometers
Transducers
  PMTs often used for high sensitivity and often cooled to reduce S/N
  CCDs for multichannel data acquisition

## Slide 14: Fluorometer

## Slide 15: Spectrofluorometer

## Slide 16: Correction of source and transducer variations with wavelength
Sources don’t have uniform power at all wavelengths which can bias excitation and emission spectra.
Most instruments have a reference spectrum stored in computer memory that can be used for instrumental correction.

## Slide 17: Pros and cons of photo-luminescent analytical methods
Photoluminescence methods are inherently more sensitive than absorbance-based measurements
  Fluorescence and phosphorescence dependent upon incident power, but measured independently of P0.
  Absorbance requires measurement of P and P0—cannot be measured independently.
  Also gives greater dynamic range because power can be modulated accordingly.
  Typically give linear calibration plots and have high selectivity.
Photoluminescent measurements have less precision and accuracy.
  Flicker noise and drift of source.
  Background fluorescence, scatter, or quenching by matrix.

## Slide 18: Applications of photoluminescence
Inorganic species determination
  Formation of fluorescent complex via chelation
  Fluorescence quenching—most common
Organic and biochemical species via fluorescence
  Valuable tool to characterize foods, pharmaceuticals, clinical samples and natural products
Phosphorimetric methods
  Complementary to fluorescent methods
    Highly phosphorescent molecules often have weak fluorescence and vice versa.
  Potentially greater selectivity because triplet conversion is required, but more difficult measurement (collisional quenching at RT problem with longer lifetimes)
Laser-induced fluorescence for detection in liquid chromatography

## Slide 19: Fluorescent lifetime measurements
Fluorecence lifetime gives added element of selectivity
  Reports on collisional deactivation and energy transfer rates proximal to the fluorophore.
  10 microsecond to sub-nanosecond time scale
http://www.olympusfluoview.com/applications/flimintro.html
http://www.oxysense.com/technology/article/how_it_works/

## Slide 20: Fluorescence microscopy
Subcellular fluorescence imaging
  Combined with recombinantly-expressed fluorophores (GFP, etc.—Roger Tsien) has revolutionized biology.
http://micro.magnet.fsu.edu/primer/techniques/fluorescence/anatomy/fluoromicroanatomy.html
http://www.rp-photonics.com/img/kahn_fl_image.jpg

## Slide 21: Fluorescence lifetime imaging (FLIM)
Cancer Research, 2005, 65, 8766-8773.
http://nimmi.bme.duke.edu/flim.html
2.4ns
1.4ns
Severe Dysplasia
Normal

## Slide 22: Chemiluminescence
Excited state that emits light generated via a chemical reaction.
  Actual mechanism usually quite complicated
Bioluminescence
  Firefly, sea pansy, jellyfish, etc.
A + B  C* + D
C*  C + hn
http://www.lifesci.ucsb.edu/~biolum/organism/photo.html

## Slide 23: Analytical applications of chemiluminescence
Typically highly sensitive because there is no other source of light noise
  “Zero background” measurement
  Very simple instrumentation
    No wavelength selection is typically needed
    Signal intensity monitored over time
Analysis of gases
  Nitric oxides: NO and NO2 via reaction with O3
Analysis of strong oxidants or species that can generate strong oxidants (enzymatically).
http://en.wikipedia.org/wiki/Luminol
http://www.kpl.com/images/WESTERN2.JPG
Luminol: 5-Amino-2,3-dihydro-1,4-phthalazinedione